## Slide 1
Embedded Workshop
Session
10

## Slide 3
Hello!
Instructor:Basma Khaled &Fatma Foley.
Cairo University, EECE Department.

## Slide 4: Content
What is SPI ?
SPI HW and SPECS
The beginning of i2c
i2c HW and SPECS
Difference between open drain and push-pull
how avr talk with spi and i2c

## Slide 5: What is SPI ?

## Slide 6
What is SPI ?
Serial Peripheral Interface (SPI) bus is a synchronous serial communication interface specification used for short distance communication.
operate with a single master device and with one or more slave devices.

## Slide 7: HW connection

## Slide 8: HW connection
SCLK : Serial Clock (output from master).
MOSI : Master Output, Slave Input (output from master).
MISO : Master Input, Slave Output (output from slave).
SS : Slave Select (active low, output from master).
Master
Slave
SCLK
MOSI
MISO
SS/CS

## Slide 9
Types of network
Independent slaves
Daisy chain
MOSI
MISO
SCK
SS0
SS1
SS2
MOSI
MISO
SCK
SS
MOSI
MISO
SCK
SS
MOSI
MISO
SCK
SS

## Slide 10: Way of communication

## Slide 11: Way of communication
It happens through shift register
master swaps a bit with the slave every clock cycle.

## Slide 12: SPECS

## Slide 13: SPECS
full duplex ,sure!!
SMMS
Serial
Synchronous

## Slide 14: Frame
It’s frameless
  No start bit
  No stop bit
  No address
  Just raw data
throughput =100%

## Slide 15: Read or Write

## Slide 16: Clock polarity
Read then write or write then read ?
who first
Sample
Setup
Sample
setup

## Slide 17: I2C

## Slide 18: The begin of I2C ”inter integrated circuit”
Need to connect between ICS
serial communication protocol at which the devices are hooked up to the I2C bus with just two wires.
Why not SPI?
two many wires
Why not UART?
communication between MCs
Is it I2C or TWI ”Two wire interface”?

## Slide 19: HW connection

## Slide 20: HW connection
SDA: serial clock Line
SCL: serial Data line

## Slide 21: Open-drain Vs push-pull

## Slide 22: What is dominant and Recessive ?
Dominant Bit: A bit that appears on the bus if any node writes it. In our system the 0 is the dominant
Recessive Bit :A bit that appears on the bus if all nodes write it. In our system the 1 is the recessive

## Slide 23: SPECS

## Slide 24: SPECS
Wired
Serial
MMMS
Half duplex
Synchronous
Throughput based on frame

## Slide 25: Frame
Start condition
SDA(falling) +SCL(High)
2) Stop condition
SDA(falling) +SCL(High)
Start condition
stop condition
Address packet
Data packet

## Slide 26
Address packet (9 bits)
  Address number (7 bits)
  R/W bit
  1 bit ack
Data packet
  Data(8bits)
  Ack
Start condition
stop condition
Address no
Data packet
W/R
ACK
Start condition
stop condition
Address no
Data
W/R
ACK
ACK

## Slide 27: Way of communication (Two scenarios)
Master writes on slave
Master read from slave

## Slide 28: SPI advanced definitions
Multi Master Arbitration
Repeated start
Clock stretching
Bus starvation

## Slide 30
Task: Use I2C protocol to interface the LCD
Using I2C communication:
Interface 16x2 LCD via I2C module
Initialize I2C peripheral
Send command and data to LCD

## Slide 31
Thank You!
Any questions?