## Slide 1
Embedded Systems Workshop
Session
4

## Slide 2
Hello!
Instructor: Mariam Ahmed.
Cairo University, EECE Department.

## Slide 4: Content
MCAL vs HAL vs APP
GPIO Registers
Input vs Output
Pull-up vs Pull-down

## Slide 5: REMEMBER
CPU
Memory
I/O Peripherals
Any computing system contains:
Notes: Know why the difference in shape between the ram and the rom (just in case someone asked)
Know how to zoom in so that ur able to show the I/O peripherals clearly

## Slide 6: REMEMBER
Registers:
Registers are small, fast storage locations inside the CPU.
Used to store (Temporary data, Control information, Results of operations).

## Slide 7: Peripherals
There are two types of registers:
On-chip peripherals
Off-chip peripherals
Timers
GPIO
ADC
Communication interfaces
Motors
LCD
Sensors
Camera

## Slide 8: Peripherals
On-chip
GPIO → buttons & LEDs
Timers → motor control
Communication → camera
Off-chip
Motors
Camera
Sensors
Drone Behaviour
Take-off / landing
Stabilization
Camera control
Notes: Ask:
Where do we write the code?
What happens if hardware changes?
What if we reuse the project?

## Slide 9
Why Layered Architecture?

## Slide 10: Layered Architecture
APP
HAL
MCAL
What is Layered Architecture?
Layered architecture is a software design approach that organizes an embedded system into multiple layers.
Each layer has a specific responsibility and interacts only with specific layers.

## Slide 11: Layered Architecture
APP
HAL
MCAL
Why Layered Architecture?
Separation and abstraction.
Easier debugging and testing.
Code reusability
Hardware independence

## Slide 12
MCAL vs HAL vs APP

## Slide 13: MCAL vs HAL vs APP
APP
HAL
MCAL
Application Layer
Hardware Abstraction Layer
Microcontroller Abstraction Layer

## Slide 14: MCAL vs HAL vs APP
APP
HAL
MCAL
Defines the overall system behaviour and application.
Provides drivers and modules for interfacing with off-chip peripherals.
Provides drivers and modules for interfacing with on-chip microcontroller peripherals.

## Slide 15
MCAL
HAL
APP
GPIO
Timers
Communication
Motors
Camera
Sensors
Take-off/Landing
Stabilization
Camera Control

## Slide 16: LIB Layer
APP
HAL
MCAL
LIB
LIB: Library layer
Provides common utility functions and definitions that can be used by all software layers.
It includes Common macros and definitions:
  Bit manipulation utilities.
  Standard data types.
Bit manipulation → BIT_MATH.h
Standard data types → STD_TYPES.h

## Slide 17
GPIO Registers

## Slide 18: ATmega32 Pin overview
There are two types of pins:
Specific purpose pins
  VCC
  GND (2 Pins)
  AVCC
  AREF
  XTAL1
  XTAL2

## Slide 19: ATmega32 Pin overview
There are two types of pins:
Specific purpose pins
General purpose pins (GPIO/DIO)
  VCC
  GND (2 Pins)
  AVCC
  AREF
  XTAL1
  XTAL2
  PORT A
  PORT B
  PORT C
  PORT D

## Slide 20: GPIO Registers
Each PORT has 3 registers:
DDR: data direction register
PORT: output data register.
PIN: input data register.
So, for each port these 3 registers for example:
Port A: A0A7, DDRA, PORTA, PINA

## Slide 21
How Do Layers Appear In Code?

## Slide 22: Code Organization Based on Layered Architecture
APP
HAL
MCAL
LIB
main.c
led.c / button.c
GPIO.c
bitmath.h / standard_types.h

## Slide 23
LIB Layer

## Slide 24: LIB Layer in Code
Compiler x
Compiler y
int x;
// int  2 bytes
int x;
// int  4 bytes
Memory explosion
Data loss

## Slide 25: LIB Layer in Code
To solve this problem, use specific data types like:
  Signed long int
  Unsigned short int
Not practical
To make it more practical and easier to deal with:
  Signed char  s8
  Unsigned short int  u16
  Unsigned long int  u32
How to achieve so in C?
Using typedef

## Slide 26: LIB Layer in Code
STD_TYPES.h file:
STD_TYPES.h is a library file that defines fixed-size, compiler-independent data types to ensure consistent memory usage across different compilers
STD_TYPES.h is located in the LIB layer.
typedef data_type new_data_name

## Slide 27: LIB Layer in Code
Bit Manipulation:
  Set bit
  Clear bit
  Toggle bit
  Get bit
  Rotate bit left/right
Why?
  Registers are controlled using bits
  Bit operations are used in all layers
  Rewriting bit logic reduces readability and safety
Set bit number 2

## Slide 28: LIB Layer in Code
Bit Manipulation using bitwise operators:
  Clear bit:
  Set bit:
  Toggle bit:
  Rotate left bit:
  Get bit:
REG |= (1<<BIT)
REG &= (~(1<<BIT))
REG ^= (1<<BIT)
(REG & (1<<BIT)) >> BIT
REG = (REG<<num) | (REG>>(8-num))

## Slide 29: LIB Layer in Code
BIT_MATH.h file:
BIT_MATH.h is a library file that provides reusable macro functions for performing bit-level operations on registers in embedded systems.
BIT_MATH.h is located in the LIB layer.

## Slide 30
MCAL Layer

## Slide 31: MCAL Layer in Code
To access any peripheral, we deal with its registers.
So, to access the GPIO we deal with the registers: DDR, PORT, PIN.
Register accessing using pointers:
To access registers, we access their addresses by using pointers:
  u8 *DDRA = (u8*) 0x3A;
  u8 *PORTA = (u8*) 0x3B;
Not practical

## Slide 32: MCAL Layer in Code
Why not practical?
Memory consumable.
* DDRA is used to access the register instead of DDRA directly.
To solve this, use #define:
#define DDRA (*(volatile u8*)(0x39))
Why volatile?
volatile prevents the compiler from caching a variable, ensuring each access reads the current value from the hardware.

## Slide 33: MCAL Layer in Code
GPIO Driver consists of two files:
GPIO.h file is a header file that contains function prototypes, macros, and configuration options for the GPIO driver.
GPIO.c file is a source file that contains the implementation of the functions declared in GPIO.h file.

## Slide 34: MCAL Layer in Code

## Slide 35: MCAL Layer in Code
For register addresses refer to Atmega 32 Datasheet, inserted table in page 327

## Slide 36
GPIO Driver

## Slide 37: STD_TYPES.h

## Slide 38: BIT_MATH.h

## Slide 39: GPIO.h

## Slide 40: GPIO.c

## Slide 41: Break

## Slide 42
Hello!
Instructor: Mohamed Magdy
Cairo University, Electrical Engineering ( EPE ) Department.
Contact me: mohamed.naem04@eng-st.cu.edu.eg
LinkedIn: https://shorturl.at/hgsIP
@ 2026 Mohamed Magdy

## Slide 43
@ 2026 Mohamed Magdy

## Slide 44
AGENDA :
Pull Up VS Pull down
Input VS Output
@ 2026 Mohamed Magdy

## Slide 45
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
Input VS Output

## Slide 46
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
In our course we will use Microcontroller AVR Atmega32.
It has 32 DIO pins grouped as following:
1- PORTA has 8 DIO Pins from A0 to A7
2- PORTB has 8 DIO Pins from B0 to B8
3- PORTC has 8 DIO Pins from C0 to C8
4- PORTD has 8 DIO Pins from D0 to D8
PORT B
PORT D
PORT A
PORT C

## Slide 47
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
PORT B
PORT D
PORT A
PORT C
Each port has 8 pins the pins of these four ports can be used as general purpose input/output (-GPIO-)
Each I/O Could be input or output (multiplexed direction).This could be controlled through the I/O port direction register

## Slide 48
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
Each MC pin could be assigned to different I/O functions. Pin Could be
configured for digital I/O, analog input, Timer I/O, Serial I/O, For example PD0
could be digital I/O or UART serial input ( Multiplexed Functionality )

## Slide 49
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
Packaging
PDIP PLASTIC DUAL IN LINE PACAKGE

## Slide 50
@ 2026 Mohamed Magdy
Each Port is controlled by 3 registers
DDRx( Data Direction Register)
This register used to decide the direction of the pins , i.e Whether the pins will act as input pins or as output pins
PORTx( Output Register )
This register is used to set the logic on the output pins HIGH OR LOW
PINx ( Input Register )
This register is used to read the logic level on the port input pins
Note : x could be A,B,C, OR D depending on which port registers are being addressed

## Slide 51
@ 2026 Mohamed Magdy
Each Port is controlled by 3 registers

## Slide 52
@ 2026 Mohamed Magdy
I/O Pin Programming Steps In AVR MC
1-Decide which pin is input and which pin is output
2-Configure the port direction use register DDRx
1 for Output.
0 for Input.
3- In Read (input case) Use register PINx
4-In write ( Output case ) Use register PORTx

## Slide 53
@ 2026 Mohamed Magdy
I/O Pin Programming Steps In AVR MC
For each output pin we can perform read/write operation on this pin .We can write on it using PORTx register and read it through PINx or PORTx register .
For each Input pin we can perform read operation only through the PINx register

## Slide 54
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
Pull Up VS Pull Down

## Slide 55
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
What is Pull-up resistor ?
Why we need it ?
How to use this feature ?
What is Pull-down resistor ?
Why we need it ?
How to use this feature ?
Pull Up VS Pull Down

## Slide 56
@ 2026 Mohamed Magdy
In case you set any PIN as input you can activate the internal pull up resistor by setting the corresponding bit in Portx register.
For each Input pin we can perform read operation only through the PINx register.
Internal Pull Up resistor
This feature is supported by all pins in the Atmega16/32 MC.
There is no internal Pull-down resistor in Atmega16/32 MC pins but it could be supported in other MC

## Slide 57
@ 2026 Mohamed Magdy
Example :
Setup pin 2 in PORTB as input and activate the internal pull up resistor
Internal Pull Up resistor
DDRB&=~(1<<2);
PORTB|=(1<<2);

## Slide 58
@ 2026 Mohamed Magdy
Lets Summarize our cases :
Internal Pull Up resistor
A PORT can have four different states depending upon the state of the bits corresponding to this pin in the data direction register (DDRx) and a data register (PORTx) of that specific port.

## Slide 59
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
4 Cases
DDxn
PORTxn
I/O
PULL-UP
Comment
0
0
1
1
O
1
0
1
I
I
O
O
NO
YES
NO
NO
TRI-STATE
( HIGH-Z )
Pxn will source current if pulled low externally
output
low ( sink )
output
high ( source )

## Slide 60
@ 2026 Mohamed Magdy
Internal Pull Up resistor
This is internal PULL-UP resistor to all the pins can be disabled by writing one to the PUD BIT IN THE SFIOR register When this is done the pins are in tri state( high impedance states ) if DDRxn =0 and PORTXN=1
Bit-2 ( PUD ) : Pull up disable
when this bit is written to one , the pull-ups in the I/O ports are disabled even if the DDxn and PORTxn Registers are configured to enable the PUll-ups

## Slide 61
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
Basics

## Slide 62
@ 2026 Mohamed Magdy
How to set values in registers ?
Set all pins of Port A AS OUTPUT
DDRA = 255;
DDRA= 0xFF;
DDRA=0b11111111;

## Slide 63
@ 2026 Mohamed Magdy
How to set values in registers ?
set all Pins in PORTA
PORTA=255;
PORTA= 0xFF;
PORTA=0b11111111;

## Slide 64
@ 2026 Mohamed Magdy
How to set values in registers ?
Clear all pins in PORTA
PORTA=0;
PORTA= 0x00;
PORTA=0b00000000;

## Slide 65
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
How to deal with a specific pin and conserving other pins ?
Set Specified bit in register
Make OR operation on the old register value with one shift left by the pin number For example if we want to set pin number 5 in PORTA
PORTA|= (1<<5);
Clear( reset ) specified bit in register
Make AND operation on the old register value with the 1 ‘s complement value of one shift left bt the pin number For example if we want to clear pin number 3 in PORTB
PORTB&=~ (1<<3);

## Slide 66
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
How to deal with a specific pin and conserving other pins ?
Toggle or Flip specified bit in register
Make XOR operation on the register old value with one shift left by the pin number for example if we want to toggle pin number 2 in PORTC
PORTC^=(1<<2);

## Slide 67
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
How to deal with a specific pin and conserving other pins ?
Check if a specified bit is set ( one )
Make AND operation on the register value with one shift left by the pin number For examlpe check if pin 2 in PORTD Is set
if( PIND&(1<<2) ) {
/*CODE*/
}

## Slide 68
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
How to deal with a specific pin and conserving other pins ?
Check if a specified bit is cleared ( reset or zero )
Just revert the previous condition For example check if pin 2 IN PORTD is cleared
if( ! ( PIND &(1<<2) ) ) {
/*CODE*/
}

## Slide 69
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
Know More about your MC
( DATA SHEET )
Sink current vs Source current
Sink current :
the sink value is the amount of current that can flow into the pin ( and therefore into the MC) safely.
Source current :
The SOURCE current is the amount of the current that can be pulled out of the pin safely.
It is very important that you try to limit the amount of current flowing into and out of your pin ( typically using series resistance )
PIN LOW
PIN HIGH

## Slide 70
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
Applications

## Slide 71
@ 2026 Mohamed Magdy
Output pins
LED AND 7-Segemnt
LCD display
Motors
Buzzer
Signal to other MC
Output to PC through PC Serial Port
Input pins
Switches ( Push button ,keypad and etc.. )
analog/digital sensors
Signal from another MC
input from PC through PC Serial Port

## Slide 72
@ 2026 Mohamed Magdy
Interfacing
Light Emitting Diode is an electrical element that emits light
by supplying a voltage difference between its terminals
LED :

## Slide 73
@ 2026 Mohamed Magdy
Interfacing
LED :
Negative Logic
Positive Logic
R= 220 : 350

## Slide 74
@ 2026 Mohamed Magdy
Interfacing
Mechanical Switch is an electrical component that can connect or break an electrical circuit.
Mechanical Switch :

## Slide 75
@ 2026 Mohamed Magdy
Interfacing
Mechanical Switch :
Switch shall be connected by pull up or pull down resistor to avoid short circuits.

## Slide 76
@ 2026 Mohamed Magdy
Interfacing
De-bonce Issue
When the Push Button is pressed the switch does not provide a clean edge The input value is bouncing for 10-30 ms
If this signal was used as an input to a digital counter for example you would get multiple counts rather than the expected single count
Sol:
1-Software
2-hardawre

## Slide 77
@ 2026 Mohamed Magdy
infinite Loop
Any C project in Embedded Systems application shall have an infinite loop called Super loop . This loop is a must even if you will leave it empty!!
Super loop used as here we have an embedded application used for a certain purpose
This loop prevents the program counter ( PC ) from continues incrementing over the flash memory and execute a garbage code.
while(1) {
/*code*/
}
for(;;){
/*code*/
}
loop:
/*code*/
gotoloop;
Most Common
Better performance
Not Good !

## Slide 78
@ 2026 Mohamed Magdy
Busy loop Delay
Software Technique to make the processor halt it’s activity for a certain time using loop.
Delay Library “util/delay.h” In AVR provides Two basic functions:
_delay_ms (value in ms);
_delay_us (value in us);
Before Using the delay library we have to define our system frequency through the F_CPU macro used by the delay library:
#define F_CPU 8000000UL 8MHZ
If not defined it will use its default frequency value which is 1Mhz

## Slide 79
@ 2026 Mohamed Magdy
@ 2026 Mohamed Magdy
TASK
• Build: Button → LED system Using layered architecture