## Slide 1
Embedded Systems Workshop
Session
4

## Slide 3
Hello!
Instructor: Mariam Ahmed.
Cairo University, EECE Department.

## Slide 4: Content
MCAL vs HAL vs APP
GPIO Registers
Input vs Output
Pull-up vs Pull-down

## Slide 5: REMEMBER
CPU
Memory
I/O Peripherals
Any computing system contains:
Notes: Know why the difference in shape between the ram and the rom (just in case someone asked)
Know how to zoom in so that ur able to show the I/O peripherals clearly

## Slide 6: REMEMBER
Registers:
Registers are small, fast storage locations inside the CPU.
Used to store (Temporary data, Control information, Results of operations).

## Slide 7: Peripherals
There are two types of registers:
On-chip peripherals
Off-chip peripherals
Timers
GPIO
ADC
Communication interfaces
Motors
LCD
Sensors
Camera

## Slide 8: Peripherals
On-chip
GPIO → buttons & LEDs
Timers → motor control
Communication → camera
Off-chip
Motors
Camera
Sensors
Drone Behaviour
Take-off / landing
Stabilization
Camera control
Notes: Ask:
Where do we write the code?
What happens if hardware changes?
What if we reuse the project?

## Slide 9
Why Layered Architecture?

## Slide 10: Layered Architecture
APP
HAL
MCAL
What is Layered Architecture?
Layered architecture is a software design approach that organizes an embedded system into multiple layers.
Each layer has a specific responsibility and interacts only with specific layers.

## Slide 11: Layered Architecture
APP
HAL
MCAL
Why Layered Architecture?
Separation and abstraction.
Easier debugging and testing.
Code reusability
Hardware independence

## Slide 12
MCAL vs HAL vs APP

## Slide 13: MCAL vs HAL vs APP
APP
HAL
MCAL
Application Layer
Hardware Abstraction Layer
Microcontroller Abstraction Layer

## Slide 14: MCAL vs HAL vs APP
APP
HAL
MCAL
Defines the overall system behaviour and application.
Provides drivers and modules for interfacing with off-chip peripherals.
Provides drivers and modules for interfacing with on-chip microcontroller peripherals.

## Slide 15
MCAL
HAL
APP
GPIO
Timers
Communication
Motors
Camera
Sensors
Take-off/Landing
Stabilization
Camera Control

## Slide 16: LIB Layer
APP
HAL
MCAL
LIB
LIB: Library layer
Provides common utility functions and definitions that can be used by all software layers.
It includes Common macros and definitions:
  Bit manipulation utilities.
  Standard data types.
Bit manipulation → BIT_MATH.h
Standard data types → STD_TYPES.h

## Slide 17
GPIO Registers

## Slide 18: ATmega32 Pin overview
There are two types of pins:
Specific purpose pins
  VCC
  GND (2 Pins)
  AVCC
  AREF
  XTAL1
  XTAL2

## Slide 19: ATmega32 Pin overview
There are two types of pins:
Specific purpose pins
General purpose pins (GPIO/DIO)
  VCC
  GND (2 Pins)
  AVCC
  AREF
  XTAL1
  XTAL2
  PORT A
  PORT B
  PORT C
  PORT D

## Slide 20: GPIO Registers
Each PORT has 3 registers:
DDR: data direction register
PORT: output data register.
PIN: input data register.
So, for each port these 3 registers for example:
Port A: A0A7, DDRA, PORTA, PINA

## Slide 21
How Do Layers Appear In Code?

## Slide 22: Code Organization Based on Layered Architecture
APP
HAL
MCAL
MCAL
main.c
led.c / button.c
GPIO.c
bitmath.h / standard_types.h

## Slide 23: LIB Layer in Code
Compiler x
Compiler y
int x;
// int  2 bytes
int x;
// int  4 bytes
Memory explosion
Data loss

## Slide 24: LIB Layer in Code
To solve this problem, use specific data types like:
  Signed long int
  Unsigned short int
Not practical
To make it more practical and easier to deal with:
  Signed char  s8
  Unsigned short int  u16
  Unsigned long int  u32
How to achieve so in C?
Using typedef

## Slide 25: LIB Layer in Code
STD_TYPES.h file:
STD_TYPES.h is a library file that defines fixed-size, compiler-independent data types to ensure consistent memory usage across different compilers
STD_TYPES.h is located in the LIB layer.
typedef data_type new_data_name

## Slide 26: LIB Layer in Code
Bit Manipulation:
  Set bit
  Clear bit
  Toggle bit
  Get bit
  Rotate bit left/right
Why?
  Registers are controlled using bits
  Bit operations are used in all layers
  Rewriting bit logic reduces readability and safety
Set bit number 2

## Slide 27: LIB Layer in Code
Bit Manipulation using bitwise operators:
  Clear bit:
  Set bit:
  Toggle bit:
  Rotate left bit:
  Get bit:
REG |= (1<<BIT)
REG &= (~(1<<BIT))
REG ^= (1<<BIT)
(REG & (1<<BIT)) >> BIT
REG = (REG<<num) | (REG>>(8-num))

## Slide 28: LIB Layer in Code
BIT_MATH.h file:
BIT_MATH.h is a library file that provides reusable macro functions for performing bit-level operations on registers in embedded systems.
BIT_MATH.h is located in the LIB layer.

## Slide 29: MCAL Layer & GPIO Driver
To access any peripheral, we deal with its registers.
So, to access the GPIO we deal with the registers: DDR, PORT, PIN.
Register accessing using pointers:
To access registers, we access their addresses by using pointers:
  u8 *DDRA = (u8*) 0x3A;
  u8 *PORTA = (u8*) 0x3B;
Not practical

## Slide 30: MCAL Layer & GPIO Driver
Why not practical?
Memory consumable.
* DDRA is used to access the register instead of DDRA directly.
To solve this, use #define:
#define DDRA (*(volatile u8*)(0x39))
Why volatile?
volatile prevents the compiler from caching a variable, ensuring each access reads the current value from the hardware.

## Slide 31: MCAL Layer & GPIO Driver
GPIO Driver consists of two files:
GPIO.h file is a header file that contains function prototypes, macros, and configuration options for the GPIO driver.
GPIO.c file is a source file that contains the implementation of the functions declared in GPIO.h file.

## Slide 32: GPIO.h file

## Slide 33
Thank You!
Any questions?